## Slide 1: Optimizing Python
Faster, Smaller, and Lower Power

## Slide 2: Why? Why are you optimizing?
Usual answer to slow scripts: “Just use C. Or, if you must, C++.”
Smaller systems
  Raspberry Pi and other single board computers
  TX2 and Nano and other SBCs that do machine learning
  CircuitPython and microcontrollers
More complicated systems
  AI with longer running times
  Video processing
Notes: InfoWorld: You answered critics who said that Python is too slow. You said every time you try to write something in Python, it is fast enough. Why is there criticism that it is too slow?
Van Rossum: What people of course do is they pick a tool and they build something incredible, and as part of the incredible thing they're building, they're doing crazy stuff, and sometimes some of the crazy stuff involves doing a whole bunch of computation, crawling through a graph of a billion social contacts or analyzing a trillion email messages or whatever.
At some point, you end up with one little piece of your system, as a whole, where you end up spending all your time. If you write that just as a sort of simple-minded Python loop, at some point you will see that that is the bottleneck in your system. It is usually much more effective to take that one piece and replace that one function or module with a little bit of code you wrote in C or C++ rather than rewriting your entire system in a faster language, because for most of what you're doing, the speed of the language is irrelevant.`

## Slide 3: What does it all mean?
Python is interpreted, not compiled. It isn’t always slower.
You should only optimize bottlenecks.
Using print to profile your code is easy though slightly fussy.
There is a built-in Python profiler that is pretty good.
Threads make code go faster but profiling harder.
Deterministic and statistical profilers each have their own place.
Visualization is to profiling as graphs are to data.
Linux tools may be more useful that Python profilers.
GPIOs and oscilloscopes are more fun anyway.
Notes: If you are nodding along to all of these and could explain them, well, you may be bored. On the other hand if you are giving me your WTF face right now, we are set, this will be great.

## Slide 4: Interpreted, not compiled
Godbolt.org
Command line, interpreter
Compiled python
Libraries: OpenCV, TensorFlow

## Slide 5: Optimize bottlenecks
Goal of profiling is to find bottlenecks
And to tell you if you’ve made it better
Not going to talk about optimizing, really, depends very much on your code.

## Slide 6: Print Profiling
Show the code
Why the prints are outside the timed areas
Ways to do this
Requires you to already have some ideas

## Slide 7: Built in profiler (s)
How to use command line
How to look at
Instrumenting functions for more info

## Slide 8: Threads, why did it have to be threads

## Slide 9: Deterministic vs Statistic
What if instead of following the processor through what it is doing, we could just ask it every once in awhile? Over enough time, it should work out.

## Slide 10: Statistical Profilers
Viz

## Slide 11: Linux tools?
top
  Remember: only optimize the bottlenecks
perf

## Slide 12: GPIOs and oscilloscopes

## Slide 13: What does it all mean?
Python is interpreted, not compiled. It isn’t always slower.
You should only optimize bottlenecks.
Using print to profile your code is easy though slightly fussy.
There is a built-in Python profiler that is pretty good.
Threads make code go faster but profiling harder.
Deterministic and statistical profilers each have their own place.
Visualization is to profiling as graphs are to data.
Linux tools may be more useful that Python profilers.
GPIOs and oscilloscopes are more fun anyway.
Notes: Questions about these?

## Slide 14: Resources
https://eng.uber.com/pyflame/

## Slide 15: Thank you!
Elecia White
Embedded: on iTunes, Spotify, embedded.fm
Logical Elegance, Inc.
Contact link on embedded.fm or contact link on logicalelegance.com